## Slide 1: CDG Horticulture, Olives & Spirits "Spirits Sector" Denatured Alcohol
Heather Jones
Unit C2 Alcohol & Tobacco
DG TAXUD
24 February 2015

## Slide 2: Denatured alcohol – Article 27 of Council Directive 92/83/EEC
Excise duty exemption applies to alcohol denatured and used in the manufacture of a product not for human consumption
The denaturants are supposed to make the product unfit for human consumption
There are 3 elements to an effective and efficient denaturant:
  A smelling agent – e.g. methyl ethyl ketone
  A tasting agent – e.g. denatonium benzoate
  A chemical analytical marker – e.g. isopropyl alcohol

## Slide 3: 2 main types of denatured alcohol
Completely denatured alcohol (CDA)
  Burning alcohol for heating, cooking and industrial cleaning alcohol
Partially denatured alcohol (PDA) – for many sectors, including:
  Cosmetics, perfumes and personal hygiene
  Screen wash, anti-freeze and de-icer
  Bio-fuels
  Paints, inks and solvents

## Slide 4: Some statistics (WHO)
30% of global alcohol is "unrecorded"
30% of that 30% is deemed to be sourced form so-called "surrogate" / i.e. denatured alcohol
Often the formulation contains methanol
Main products abused are:
  Screen wash, anti-freeze, de-icer
  Cheap perfume, aftershaves, any strong alcohol mouthwashes
  Even nail varnish remover

## Slide 5: What's the problem?
Still too many existing national / weaker formulations for both CDA and PDA
Ease of removability of those weaker methods to return the alcohol to a potable state
Some approved denaturants are just flavours, aromas and essential oils making the potential for fraud even easier – no cleaning up necessary
  E.g rose oil, citrus, orange, cucumber, menthol

## Slide 6: How easy / cheap is it to clean up denatured alcohol?
It is very easy / inexpensive with a weak denaturing formulation
The "Euro" CDA formulation implemented in July 2013 is very robust but is deemed too costly by industry so take up has been disappointing
The removability tests show that all the national formulations which do not have a chemical marker are very easy to clean up

## Slide 7
Removability tests using activated carbon – Simple adsorption tests
Activated carbon - NORIT GCN 1240 PLUS - 3.5 Euros / kg
VWR activated charcoal
(Fine powder)
25 g / 100 mL (EtOH 50%)
Norit GCN1240 PLUS
(Granular AC / Coconut shell)
25 g / 100 mL (EtOH 50%)

## Slide 8
Removability tests on CDA and screenwash using preparative columns packed with activated carbon
Packing: 20 g Norit + 5 g VRW charcoal / 100 mL EtOH (ca. 50%)

## Slide 9: Screenwash – GC-FID analysis before / after activated carbon treatment

## Slide 10: Aftershave – sold at retail for < 1€ for 250ml, contains 64% ABV alcohol and lemon or cucumber as the "denaturant"

## Slide 11: Products don’t need cleaning up - consumed as they are

## Slide 12: Some more examples…

## Slide 13: Is this a problem only in certain Member States? Recent fraud case involving anti-freeze (UK)

## Slide 14: Brand - German labelling?
Bar codes?
Concentrate or diluted?
Who's denaturing formulation?

## Slide 15: Lost revenues, health risks, legitimate brands abused, consumers mis-led
Recent case from the UK (Leicester, Dec 2014)
25 x pallets of 1,080 well known branded vodka bottles = 27,000
243 x empty 5l bottles of anti-freeze (German labelling) = 1,215 litres prior to extraction/watering down
Large quantity of cardboard branded vodka boxes
Large quantity of branded bottle tops
2 x Reverse Osmosis units to remove the colour and fragrance from the
product
1 x water softener unit as assist in the dilution

## Slide 16: What is being done?
DG TAXUD and DG Joint Research Centre (JRC) working together on the denaturant project
Now phase 3 – screen wash / anti-freeze
Need to continue to work legitimate spirits industry to collect more data on fraud
Possibilities under Article 27 (5) to report cases of fraud , avoidance and abuse
A study on the "structures" Directive has just started – Article 27 will be a priority

## Slide 17: The Study – Council Directive 92/83/EEC
An evaluation of the effectiveness, efficiency, relevance and coherence of the provisions of the Directive
Priorities based on initial understanding of problem areas:
  Article 27 – exemptions
  Also looking at classification, reduced rates
  Other reported issues

## Slide 18: Evaluation of Directive 92/83/EEC
Notes: <number>

## Slide 19: Timeline
Kick Off meeting Jan 2015
Inception until beginning Mar 2015
Steering Group (1) Mar 2015
Fiscalis Seminar May 2015
Steering Group June 2015
FPG June 2015
Progress report Aug 2015
Draft final report Oct 2015
Steering Group Oct 2015
FPG Oct 2015
Final report Dec 2015
Follow up 2016-2017
– possible impact assessment / proposal

## Slide 20: Other initiatives
Food Integrity Project (spirits work programme) – DG RTD. Authenticity – through chemical analysis
Clear synergies with the denaturant project:
  Developing IT tools, such as hand held detection techniques for faster testing
  Standard Operating Procedures (SOP) for all the customs laboratories
  Early warning systems for tracing illicit alcohol (e.e. mapping tools exist in some MS – UK and LT)
Tracing back the product to the denaturant and the MS is key.
The more denaturing methods there are – the greater the risk!

## Slide 21: Thank you